Recognized verbal instructions for 手元TEMOTO teleoperator

Operator input

NATURAL CONTROL MODE
Operator's hand and robot's end effector are considered to be oriented the same way.

INVERTED CONTROL MODE
Left and right are inverted for operator's hand and robot's end effector.

IGNORE ROTATION
Hand rotation (orientation) is not transferred to robot's end effector, i.e. the rotation of the end effector	will not be altered.

CONSIDER ROTATION
Hand rotation (orientation) will be considered when setting a target pose for the end effector.

LIMIT DIRECTIONS
Only displacement in certain direction(s) is considered when setting a target pose for the end effector.

FREE DIRECTIONS
Displacement of the operator's hand in any direction will be considered when setting a target pose.

MoveIt!

ROBOT PLEASE PLAN
Start the planner for moving the end effector to the pose determined by operator's hand.

ROBOT PLEASE EXECUTE
Execute the latest plan available.

ROBOT PLEASE GO
Start the planner and execute right after. Equivalent of Plan & Execute.

ROBOT PLEASE PLAN HOME
Start the planner for returning to a saved home pose.

ROBOT PLEASE GO HOME
Plan and execute the return to the saved home pose.